## Slide 1: CS105 Introduction to Computer Concepts GATES and CIRCUITS
Instructor: Yang Mu

## Slide 2
How computers use electric signals to represent and manipulate binary values?
Notes: Any given electronic signal has a level of voltage. As we mentioned in the
last chapter, we distinguish between the two values of interest (binary 0
and 1) by the voltage level of a signal. In general, a voltage level in the
range of 0 to 2 volts is considered “low” and is interpreted as a binary 0.
A signal in the 2- to 5-volt range is considered “high” and is interpreted as
a binary 1. Signals in a computer are constrained to be within one range or
the other.

## Slide 3: Outline
Gates
  Types
  Construction
Circuits
  Adder
  Multiplexer
  Memory
  IC

## Slide 4: Computers and Electricity
Definitions:
  Gate: A device that performs a basic operation on electrical signals
  Circuits: Gates combined to perform more complicated tasks
How do we describe the behavior of gates and circuits?
  Boolean expressions: Uses Boolean algebra, a mathematical notation for expressing two-valued logic
  Logic diagrams: A graphical representation of a circuit; each gate has its own symbol
  Truth tables: A table showing all possible input value and the associated output values

## Slide 5: Gate Types
Six types of gates
  NOT
  AND
  OR
  XOR
  NAND
  NOR

## Slide 6: NOT Gate
A NOT gate accepts one input signal (0 or 1) and returns the opposite signal as output
Figure 4.1 Various representations of a NOT gate

## Slide 7: AND Gate
An AND gate accepts two input signals
If both are 1, the output is 1; otherwise, the output is 0
Figure 4.2 Various representations of an AND gate

## Slide 8: OR Gate
An OR gate accepts two input signals
If both are 0, the output is 0; otherwise, the output is 1
Figure 4.3 Various representations of a OR gate

## Slide 9: XOR Gate (exclusive OR)
Figure 4.4 Various representations of an XOR gate
An XOR gate accepts two input signals
If both are the same, the output is 0; otherwise,
the output is 1

## Slide 10: NAND Gate
The NAND gate accepts two input signals
If both are 1, the output is 0; otherwise, the output is 1
Figure 4.5 Various representations of a NAND gate

## Slide 11: NOR Gate
Figure 4.6 Various representations of a NOR gate
The NOR gate accepts two input signals
If both are 0, the output is 1; otherwise,
the output is 0

## Slide 12: Gates with More Inputs
Gates can be designed to accept three or more input values
A three-input AND gate, for example, produces an output of 1 only if all input values are 1
Figure 4.7 Various representations of a three-input AND gate

## Slide 13: Constructing Gates
Transistor
A device that acts either as a wire that conducts electricity or as a resistor that blocks the flow of electricity, depending on the voltage level of an input signal
A transistor has no moving parts, yet acts like a switch
It is made of a semiconductor material, which is neither a particularly good conductor of electricity nor a particularly good insulator

## Slide 14: Constructing Gates
A transistor has three terminals
  A source
  A base
  An emitter, typically connected to a ground wire
If the electrical signal is grounded, it is allowed to flow through an alternative route to the ground (literally) where it can do no harm
Figure 4.8 The connections of a transistor

## Slide 15: Constructing Gates
The easiest gates to create are the NOT, NAND, and NOR gates
Figure 4.9 Constructing gates using transistors

## Slide 16: Circuits
Combinational circuit: The input values explicitly determine the output
Sequential circuit: The output is a function of the input values and the existing state of the circuit

## Slide 17: Combinational Circuits
Gates are combined into circuits by using the output of one gate as the input for another

## Slide 18: Combinational Circuits
Consider the following Boolean expression A(B + C)
Does this truth table look familiar?
Compare it with previous table

## Slide 19: Combinational Circuits
Circuit equivalence
Two circuits that produce the same output for identical input
Boolean algebra allows us to apply provable mathematical principles to help design circuits
E.g., A(B + C) = AB + BC (distributive law) so circuits must be equivalent

## Slide 20: Adders
At the digital logic level, addition is performed in binary
Addition operations are carried out by special circuits called, appropriately, adders

## Slide 21: Adders
The result of adding two binary digits could produce a carry value
Recall that 1 + 1 = 10 in base two
Half adder
A circuit that computes the sum of two bits and produces the correct carry bit
Truth table

## Slide 22: Adders
Full adder
A circuit that takes the carry-in value into account
Figure 4.10 A full adder

## Slide 23: Multiplexers
Multiplexer
A circuit that uses a few input control signals to determine which of several output data lines is routed to its output

## Slide 24: Multiplexers
The control lines S0, S1, and S2 determine which of eight other input lines
(D0 … D7) are routed to the output (F)
Figure 4.11 A block diagram of a multiplexer with three select control lines

## Slide 25: Circuits as Memory
Digital circuits can be used to store information
These circuits form a sequential circuit, because the output of the circuit is also used as input to the circuit

## Slide 26: Circuits as Memory
An S-R latch stores a single binary digit (1 or 0)
There are several ways an S-R latch circuit can be designed using various kinds of gates
Figure 4.12 An S-R latch

## Slide 27: Circuits as Memory
The design of this circuit guarantees that the two outputs X and Y are always complements of each other
The value of X at any point in time is considered to be the current state of the circuit
Therefore, if X is 1, the circuit is storing a 1; if X is 0, the circuit is storing a 0
Figure 4.12 An S-R latch

## Slide 28: Integrated Circuits
Integrated circuit (also called a chip)
A piece of silicon on which multiple gates have been embedded
Silicon pieces are mounted on a plastic or ceramic package with pins along the edges that can be soldered onto circuit boards or inserted into appropriate sockets

## Slide 29: Integrated Circuits
Integrated circuits (IC) are classified by the number of gates contained in them

## Slide 30: Integrated Circuits
Figure 4.13 An SSI chip contains independent NAND gates

## Slide 31: In class exercise
Write down the truth table for XOR
Of what is a transistor usually made?
Show the behavior of the following
circuit with a truth table: